## Slide 2: HOM couplers for crab cavities and challenges
TTC 2020
James Mitchell
CERN, BE-RF-PM
james.mitchell@cern.ch
BE-RF-PM

## Slide 3: Crab cavity damping
Double Quarter Wave (DQW)
Radio Frequency Dipole (RFD)
1 x H-HOMC
1 x V-HOMC
1 x Field Antenna
1 x HF Damper
1 x Field Antenna
3 x HOM Coupler
Damping requirements:
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 4: Crab cavity damping
TTC 2020
james.mitchell@cern.ch
BE-RF-PM
S. Verdu-Andres
Dressed cavities tested without beam.
Dressed DQW tested with beam!

## Slide 5: Topics
TTC 2020
james.mitchell@cern.ch
BE-RF-PM
Dynamic heat loads (gasket heating)
Change of characteristic impedance (Z0)

## Slide 6: Dynamic Heat Loads
Dynamic heat load on gaskets reduced by:
Rejection filter before the gasket.
 complicated geometry
 high fields on hook
broad notch (mW level heat-load)
Waveguide with fc > 400 MHz
 hard to machine and weld
 higher nominal gasket heat-load
 less sensitive to tolerances
ωc
Could complex couplers and cavity shapes could be avoided with SC seals?
a
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 7: Dynamic Heat Loads
Dynamic heat load on gaskets could be reduced by: Superconducting seals*.
Resulting in more ‘manufacturable’ cavities and couplers.
Material | Rs @ 2 K [Ohms]
Copper | ~ 1 e-3
Niobium | ~ 20 e-9
We are trialing several options for tests!
Future high energy machines  mass production.
Do superconducting seals allow simplification of cavity and coupler geometries?
TTC 2020
james.mitchell@cern.ch
BE-RF-PM
*Existing literature on the use of superconducting seals in back-up slides.
On DQW the copper gasket heat-load is 2-20 W

## Slide 8: Changing Z0: Manufacture and Transport
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 9: Changing Z0: 50 Ω  25 Ω
… concerns over thin diameter in feedthrough.
Changed to Z0 = 25 Ω.
Z0 [Ω] | ID [mm]
75 | 0.78
50 | 2.90
25 | 10.77
Transported in horizontally position.
Large moment on thin inner conductor!
M
*
* Approximation without taking into account the boundary conditions of the ceramic.
Since , diameter increases by factor of 3.7 if we move to 25 Ω.
Bending stress reduces by at least factor of 30.
*
TTC 2020
james.mitchell@cern.ch
BE-RF-PM
Shock test results and videos in back-up slides!

## Slide 10: Changing Z0: 50 Ω  25 Ω
Chose 25 Ω, because 25 Ω = 50 Ω || 50 Ω
Feedthroughs designed.
There is now a common 25 Ω feedthough validated with thermal shock and ‘drop test’.
With the steps and clearances needed for manufacture.
Inner diameter of 14 mm gave best broadband matching!
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 11: Changing Z0: 50 Ω  25 Ω
DQW HOM coupler
  Decrease in transmission at high power mode frequency (960 MHz).
  Re-tuned - now impedance for this mode is the lowest it has been!
Design thresholds are met with 25 Ohm matching for both cavities!
Cavity impedances in back-up slides.
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 12: Changing Z0: 50 Ω  25 Ω
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 13: Changing Z0: 50 Ω  25 Ω
Infrastructure and measurement challenges.
  25 ohm cables and loads are not standard: Make cables of match in parallel?
  Using a 50 Ω VNA: port re-normalization, de-embedding, 50 Ω 25 Ω adapters.
Port renormalization built into new VNAs!
TTC 2020
james.mitchell@cern.ch
BE-RF-PM
WARNING:
Must de-embed adapter to 25 ohm section!

## Slide 14: Conclusions and Discussion points
TTC 2020
james.mitchell@cern.ch
BE-RF-PM
Dynamic heat loads
We have reduced H-field.
Could reduce Rs.
Could this lead to simpler structures?
Is there a want for this in the accelerator community?
Z0 = 25 Ω
Inner conductor is too thin for transport.
25 Ohm infrastructure designed.
Impedance thresholds met.
Challenges: infrastructure and measurements.
R&D on-going!
Baseline for crab cavities

## Slide 15: Thank you for listening!
TTC 2020
james.mitchell@cern.ch
BE-RF-PM
Thanks to BE-RF-PM and HL-LHC WP4 for the contribution and support.

## Slide 16: Back-up slides
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 17
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 18
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 19
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 20
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 21: Changing Z0: 50 Ω  25 Ω
‘Shock tests’ on-going.
25 ohm feedthrough was shown to be more resistant to a shock!
Brazing issue:
Wall thickness limitation.
TTC 2020
james.mitchell@cern.ch
BE-RF-PM

## Slide 22: High Power HOMs
Coaxial line power is becoming comparable to FPC power.
Infrastructure for HOM couplers is becoming larger and more difficult to assemble/replace.
What will be the best damping method for future machines?
 | Pworst-case (Paverage) [kW] | 
 | Gaussian bunch | Binomial bunch
DQW | 1.0 (0.2) | 0.5 (0.1)
RFD | 7.4 (0.8) | 5.9 (0.7)
Using HL-LHC beam parameters:
HOM power from 10,000 stochastic simulations.
Parameters: bunch length, bunch form coefficient, mode frequencies and mode Q-factors.
Worst case power at these frequencies.
RFD
DQW
TTC 2020
james.mitchell@cern.ch
BE-RF-PM
Notes: LCLS II: FPC  6 kW

## Slide 23: ImageGen
CD
OD
T
ID
TTC 2020
james.mitchell@cern.ch
BE-RF-PM